## Slide 1: Advanced Drivetrain Calculations
John E. V-Neun, Team 229
John A. Neun, P.E., Team 20
Notes: Thank you for taking the time to listen to us talk about robot transmissions.
My name is John Neun, and this is my son John V-Neun.
I have been an engineer for about 30 years now, and it is a great and rare opportunity to give a technical presentation with my son. I went to Rensselaer Polytechnic Institute, the oldest civilian engineering school in the US. John is about to graduate from Clarkson University, and I am now suffering my new identity, “John V-Neun’s Dad.”
I’ll do a somewhat formal presentation of some material, John will do a spreadsheet demo, and there should be plenty of time for discussion either during or after.

## Slide 2: Goals for this Session
Foundation for Gearbox Design
Review principles in drivetrain design
Examine trade-offs
Formulas for modeling and design
Sample Calculation
Notes: We would like to build on the presentation on drive system fundamentals done by the now two Woody Flowers award winners, Ken Patton and Paul Capioli. Essentially, we will add a little mathematics to the process after reviewing some basic principles, and then present a tool in the form of a spreadsheet to implement these ideas. I’ll review some slides outlining the physics, and John will do an example with his spreadsheet. In case you haven’t figured this out, he is the real brains behind this operation.

## Slide 3: Prerequisites
Assume basic familiarity with:
  Principles of Physics and Calculus
    Forces, Power, Torque, Acceleration, Friction, Rotational vs. Linear Motion
  Principles of DC Motors
  Principles of Gear Trains
  Ken and Paul’s seminar
Notes: Paul and Ken revieweed all of thi stuff, and I will not presume to teach you about torque, power, or Newtonian laws of motion. I suspect you all understand this stuff at least as well as I do.

## Slide 4: Gearbox Design Process
Determine maximum
drive train load from
“wall push”
Motor running
characteristics
Max torque per
current limit
Pick motor
  (load vs amps)
Pick wheel config.
  no. of wheels
  material
  diameter
Calculate required gear
ratio from motor and
output torques
Calculate speed
& acceleration
Running characteristics
Current limits
Iterate
First, choose “Motion” Objective: Robot Speed 13 fps, full speed within 10 feet
Notes: The first thing to do is to choose the “motion” objective. This really means the you need to understand how fast and how strong you want your robot to go. Next, you need to choose both ends of the drive train. That is, the motor or these days motors, and the “ground effector.” Somewhere between the wheels and the motor, there’s usually a gearbox or transmission. This process characterizes each of those, and then develops a means to reconcile and connect the two. I’ll review these steps.

## Slide 5: Transmission Goal: Translate Motor Motion and Power into Robot Motivation
Motor
  Speed (rpm)
  Torque
Robot
  Speed (fps)
  Weight
Notes: Therefore, a gearbox or transmission is a device to translate motor motion into wheel and ultimately robot motion. With some basic parameters or assumptions about each of those, you can design a good transmission.

## Slide 6: First Analysis Pushing against a wall…
Objective: Determine maximum load limit
System must withstand max load
  Run continuously under maximum load
  Not overload motors
  Not overload circuit breakers
  (Not break shafts, gears, etc.)
Suboptimum – ignore limit (risk failure)
Notes: How do you characterize this stuff? First, determine the limit of the motor. This sets the bounds of the system.

## Slide 7: Pushing against a wall…
Known Factors:
  Motor Usage
    Motor Characteristics
  Wheel Friction
  Max Motor Load (at 40 amps)
Solve For:
  Required Gear Ratio
Robot Weight
Motor specs
Frictional coef.
Speed
acceleration
Gear Ratio
Notes: “Pushing against a wall” implies determination of the ultimate stall load of the motor, and the maximum load that the robot can impart on the motor. The first is a function of the motor. The second is mostly a function of the weight of the robot and wheel geometry and traction material.

## Slide 8: Max Motor Load
TL = Torque from load
IM = Maximum current draw (motor limit)
Ts = Stall torque
IF = Motor free current
IS = Motor stall current
Notes: What about a motor determines its limits? A DC motor has two ultimate points of operation. The first is at zero rpm, a stall condition. The second is its free speed, the speed at which theoretically no load is applied to the shaft. At stall, motor load is maximum, and at free speed, motor load is minimum. Of course, there is no such thing as “no load.” There is always some power consumed to overcome windage, friction, and other parasitic effects. Thus, there is some current associated with this free speed. You can simply assume a straight line between the two. If there is a current limit imposed by a system constraint like, for example, a circuit breaker, you can calculate the torque associated with that limit with the assumed line between stall and free speed with this simple interoplative equation.

## Slide 9: Calculate the Max Motor Load
stall
Free speed
Notes: Here is a simple illustration of these concepts. These lines are not really perfectly straight, but for our purposes, the assumption is adequate.

## Slide 10: Calculate the Gearbox Load Find Required Gearbox Ratio
Friction between wheel and carpet acts as a “brake”, and provides gearbox load.
Find torque load per gearbox.
Now Solve for Required Gear Ratio
Weight
no. of wheels
Frictional force
Notes: From the wheel side, we need to know what the “break away” frictional load is, and then using the wheel circumference, converting that to a torque. The gear ratio is simply the ratio of the axle load and motor load.

## Slide 11: Check Robot Speed
How fast will the robot go with this required gear ratio?
Remember Units!!!
Notes: Now the other half of the equation. We have bounded the gear ratios with load. They also determine speed. Is the robot fast enough?

## Slide 12: Is this fast enough?
Major Design Compromise…
Is this speed fast enough?
No?
  Decrease Gearbox Load
  Increase Gearbox Power
  Live with the low speed…
  Design two speeds!
    Low speed/high force
    High speed/low force
  Risk failure
Design is all about tradeoffs
Notes: Is the machine fast enough? If not, then you can make the wheels slip earlier, put on more power to lessen the reduction, live with it, or design two gear boxes in one.

## Slide 13: Secondary Analysis Plotting Acceleration
Calculate Motor Current Draw and Robot Velocity over time (during robot acceleration).
Time to top speed
  Important to show how drivetrain will perform (or NOT perform!)
  If a robot takes 50 feet to accelerate to top speed, it probably isn’t practical!
Notes: Now, how long does it take for the machine to get to speed?

## Slide 14: Plotting Acceleration
Voltage to resting motor
  Start at stall condition (speed = 0)
  Stall torque  initial acceleration
Robot accelerates
  Motor leaves stall condition
  Force decreases as speed increases.
Notes: The machine acceleration rate also determines how long the robot will spend at that “infinite” torque. Too long, and breakers start to trip. Remember those lines relating speed, torque, and load?

## Slide 15: Instantaneous Motor Torque
When Motor RPM = 0,
Output Torque = Stall Torque
When Motor RPM = free speed
Output Torque = 0 (in theory)
(.81)
Notes: To calculate instantaneous torque, you just interplate on that assumed straight line between stall and free speed.

## Slide 16: Gearbox Torque Output Robot Accelerating Force
Notes: Output torque, converted to a force across the wheels, determines acceleration.

## Slide 17: Instantaneous Acceleration and Velocity
Instantaneous Acceleration (dependant on robot velocity, as seen in previous equations).
The instantaneous velocity can be numerically calculated as follows:
(thanks, Isaac)
Notes: We all learned this stuff in the first week or two of Physics I. F=ma, and V = at.

## Slide 18: Velocity vs. Time
The numerical results can be plotted, as shown below (speed vs. time):
Notes: It is easy to “spreadsheet” these relations, and plot the results. Speed comes to some steady state in some finite time.

## Slide 19: Current Draw Modeling
The current drawn by a motor can be modeled vs. time too.
Current is linearly proportional to torque output (torque load) of the motor.
Notes: We then move back to the other assumed line between current limits, and figure out if we are ok.

## Slide 20: Current Draw vs. Time
The numerical results can be plotted, as shown below:
Notes: We come to some equilibrium current draw at speed. Power is of course voltage times current.

## Slide 21: What does this provide?
Based on these plots, one can see how the drivetrain will perform.
  Does current draw drop below “danger” levels in a short time?
  How long does it take robot to accelerate to top speed?
Notes: Does it work?

## Slide 22: Are things okay? NO?!?
How can performance be increased?
  Increase Drivetrain Power
    Use Stronger Motors
    Use Multiple Motors
  Increase Gear Ratio (Reduce top speed)
    Is this acceptable?
Notes: How to iterate.

## Slide 23: Adding Power – Multiple Motors
Combining Motors Together – Not Voodoo!
  2 Motors combine to become 1 “super-motor”
  Match motors at free speed.
  Sum all characteristics
    Motor Load is distributed proportional to a ratio of free speed.
  2 of the same motor is easy!
    4 Chiaphua Motors

## Slide 24: Multiple Speed Drivetrains
Allows for one “pushing” gear, and one “cruising” gear.
Shift on the fly allows for accelerating through multiple gears to achieve high speeds.
Shifting optimizes motor power for application at hand.

## Slide 25: The big picture…
These calculations are used to design a competition drivetrain.
Rather than do them by hand, most designers use some kind of tool.
  Excel Spreadsheet
  Matlab Script
  Etc…

## Slide 26: And then…
This is a starting point
  Iterate to optimize results
  Test
Use your imagination
  Infinite speeds
  Multiple motors
  Many gears
  This isn’t the “end all” method.

## Slide 27: Gearbox Design Process
Determine maximum
drive train load from
“wall push”
Motor running
characteristics
Max torque per
current limit
Pick motor
  (load vs amps)
Pick wheel config.
  no. of wheels
  material
  diameter
Calculate required gear
ratio from motor and
output torques
Calculate speed
& acceleration
Running characteristics
Current limits
Iterate
Set “Motion” Objective: Robot Speed 13 fps, full speed within 10 feet

## Slide 28: Demonstration
Here is an example of how to use a spreadsheet to do drivetrain design.
  www.team229.org
  Everything is available (or soon will be) in resources section of 229 web site

## Slide 29: Calculation Demonstration