## Slide 1: Mechanisms
Paul Ventimiglia
WPI Student, Team 190

## Slide 2: Overview Manipulating Game Objects
Collection Systems
  Intake Rollers
  Conveyors
  Claws
  Fixed, passive devices
Positioning Methods
  Arms (rotating)
  Telescoping lifts
  4-bar mechanisms

## Slide 3: Look at your object!
Answer these questions first
  Is it heavy?
  Does it take up a large space?
  Is it fragile?
  Does the orientation matter?
  Where is it? (floor, platform, human player)

## Slide 4: Intake Rollers
Rotating cylinders designed to contact and move your game object
Commonly used to pick up balls from the floor
Horizontal or vertical

## Slide 5: Intake Rollers

## Slide 6: Intake Rollers
Advantages
  Lightweight
  Pickup multiple objects quickly
  Large room for driver error
  Simple
    Few parts to break
Disadvantages
  Works best for balls
  Conveyors difficult to stay on reliably
  Can cause jamming
  Requires chassis space near floor

## Slide 7: Conveyors
Effective with rollers at picking up and MOVING objects
A flat, wide, moving belt
Series of smaller belts in parallel

## Slide 8: Examples

## Slide 9: Claws
Appendages which open and close to grasp onto an object
“fingers” rotating to close around an object
“fingers” move towards each other to clamp onto an object
Any orientation, can pick up almost everything

## Slide 10: Claws

## Slide 12: Claws

## Slide 13: Claws
Advantages
  Lightweight
  Grab very large objects
  Grab strangely shaped objects
  Easiest to build without machine tools
Disadvantages
  Work best with pneumatics
  Take up large volume often
  Require good drivers and careful positioning
  Only pick up one object at a time

## Slide 14: Examples

## Slide 15: Fixed Devices
KISS!
A simply shaped device that interacts with the object
Useful only if object has something to grasp onto

## Slide 16: Fixed Devices
Advantages
  Lightweight!
    More weight to make other parts work better
  Reliable
    No moving parts break
  Cheapest and easiest to manufacture
Disadvantages
  Only work with certain objects
  Limited ability
    Relies upon skill of driver and specific setups
  No room for adaptability in a match

## Slide 17: Arms (rotational lift)
Consist of one or more points of rotation
Manipulator on the end of an arm
Versatile and effective
Lift objects high simply

## Slide 18: Arms (rotational lift)

## Slide 19: Shoulder Joint

## Slide 20: Adding a Wrist

## Slide 22: Arms (rotational lift)
Advantages
  Mechanically reliable for most heights
  A shoulder and wrist provide excellent control
  Can reach over robots and still fold up
  Multiple functions
  Can be built simply!
    Capstans
    Sprocket and chain
Disadvantages
  Requires high strength parts
  Can raise CG too high
  Must fit into starting size limit
  Can require careful strategy not to hurt other robots

## Slide 23: Examples

## Slide 24: Telescoping
Sliding sections that move linearly
Mostly powered by a winch pulling on a cable
Similar to the front of a forklift

## Slide 25: (images from Greg Needel’s presentation on the FIRST website)

## Slide 27: Telescoping
Advantages
  Able to extend very far with little space consumed
  Stable linear path
  Less for driver to think about
  Simply powered by a winch
Disadvantages
  Jamming, they jam, and jamming too.
  Hard to repair
  Require being stored in a long straight area
  Do not handle bending loads well

## Slide 28: Examples

## Slide 29: 4-Bar linkages

## Slide 30: (images from Greg Needel’s presentation on the FIRST website)

## Slide 31: 4-Bar (rotational lift)
Advantages
  Controls orientation of arm and object
  Complex motion from a simple input
  Simple to implement
Disadvantages
  Limited range of motion
  More moving parts
  Over center toggling
  Certain links can require lots of torque

## Slide 32: Design Selection
How high does the object need to be lifted?
  Arm with 1 joint vs. elevator with 1 section, etc
Does the robot need to fit under an obstacle?
  Arm folded down vs. telescoping arm with a pivot
How much weight and space is there for it?
  A conveyor system blocks half the robot vs. must weigh less than 10lbs and lift 10ft high
Prioritize first!

## Slide 33: Materials
Steel
  Axles, pins, bolts
Aluminum
  Structural shapes, plates, axles
Plastics
  Lighter parts, complex shapes, covers

## Slide 34: Transmission
Sprockets and chain
  #25, #35
Gears
  ~20 pitch to ~12 pitch
Urethane round belts
Timing belts and timing pulleys
Capstans

## Slide 35: Vendors
Mcmaster.com
  All transmission parts and materials
Onlinemetals.com
  Aluminum structural
Sdp-si.com
  transmission
Banebots.com
  Gearboxes
Robotmarketplace.com
  Gearboxes
Home Depot
  Small amounts of aluminum tubing

## Slide 36: Questions?
(super excited about mechanism building)