## Slide 1: Pneumatic Power
Presented by:
Raul Olivera, WildStang - 111

## Slide 2: Outline
Some Basics of Pneumatics and Associated Physics
  Pressure - Absolute & Gage
  Force, Pressure & Area
  Air Properties
  Flow Rates
  Electrical Analogy
  Mechanical Power & Work
  Pneumatic Energy & Power
Managing Pneumatic Energy Capacity
Power Experiment
Pneumatics vs. Motors

## Slide 3: Pressure - Absolute & Gage
Pressure = matter pushing against matter
  Object pushing against another object
Absolute (psia) => True matter based pressure
  0 psia => no matter present to press against objects
  Not too important in our designs
Gage (psig) => Relative to Atmosphere
  0 psig => pressure in equilibrium with atmosphere
  All regulators and gauges based on this

## Slide 4: Force, Pressure & Area
Pressure = Force / Area
Force = Pressure X Area
Example: 30 psig in 2” diameter cylinder
30 psig
2.0” dia.
Force = 30 psi X 3.14 sq-in = 94.2 lbs
Area = r2 = (1”)2 = 3.14sq-in
94.2 lbs

## Slide 5: Some Basic Properties of Air
Compressible
Higher Pressure = Higher Friction
Ideal Gas Law:
  PV = nRT
  Pressure is proportional to Temperature
  Pressure is inversely proportional to Volume

## Slide 6: Pressure & Volume

## Slide 7: Flow Rates
Flow rate = Volume / time
  i.e. CFM (L/min, cu-in/sec)
Flow Controls - Valves
  Solenoid Value
  Check Valve
  Relief Valve
  Flow Control Valve
Unintended Flow Restrictions:
  Narrow Passages
  Flow Friction
  Pressure drops while it is flowing due to restrictions

## Slide 8: Electrical Analogy
Pressure = Voltage
Volume = Capacitance
Flow rate = Current
Flow Restrictions = Resistance
HOWEVER: Air is compressible
  => Some unique non-linearities when compared to electrical systems

## Slide 9: Mechanical Power & Work
Work = Force x Distance (in-lb)
  Also Work = Torque x Revolutions
  Mechanical Energy is always involved in doing work
    It is transferred or converted
Power = Work / Time (in-lb/s)
  or Energy / Time
Power Concept
  How far a resisting object can be moved in a given time
  The power rating of motors is what allows us to determine which ones can be used for a given job
Power rating for pneumatic actuators?
  Depends greatly on the rest of the pneumatic system

## Slide 10: Pneumatic Energy & Power
Energy = Force x Distance
  Force = Pressure x Area
  Distance = Volume / Area
  Energy = Pressure x Volume
    ( psig x cu-in => in-lbs )
Power = Energy / Time
  Power = Pressure x Volume / Time
    ( Units = in-lbs )
  Flow rate = Volume / Time
  Power = Pressure x Flow rate
    ( Psig x cu-in/sec => in-lbs/sec )
PEU =
Pneumatic
Energy
Units

## Slide 11: Managing Pneumatic Energy Capacity
Pneumatic Energy Capacity = Volume of Pressurized Air
  Managing the loss and addition of pressurized air is very important
  WHY - the volume of air used in large cylinders could deplete your supply very quickly if not managed

## Slide 12: Managing Pneumatic Energy Capacity
Store Pneumatic Energy
  Storage Tanks
  Tubing, Fittings & Valves
  Compressor
Consume Pneumatic Energy
  Exhaust of actuators
  Leakage
Add Pneumatic Energy
  Activate compressor

## Slide 13
120 psig
60 psig
120 PSI Side |  |  | 60 PSI Side |  |  | 
PEU | P | V | P | V | PEU | Tot PEU
2400.0 | 120.0 | 20.0 | 60.0 | 10.0 | 600.0 | 3000.0
1800.0 | 90.0 | 20.0 | 60.0 | 10.0 | 600.0 | 2400.0
1200.0 | 60.0 | 20.0 | 60.0 | 10.0 | 600.0 | 1800.0
800.0 | 40.0 | 20.0 | 40.0 | 10.0 | 400.0 | 1200.0
533.3 | 26.7 | 20.0 | 26.7 | 10.0 | 266.7 | 800.0
355.6 | 17.8 | 20.0 | 17.8 | 10.0 | 177.8 | 533.3
Energy Capacity Example

## Slide 14: The Compressor - Published Performance
Averages about 660 PEU/s in the cut out range (90 to 120 psig)

## Slide 15: The Compressor - My experiment
Averages about 110 PEU/s in the cut out range (90 to 120 psig)

## Slide 16: Managing Pneumatic Energy Capacity
Energy Capacity Example - AGAIN:
  Storage Tanks
    => Energy Capacity = 4524 (2 tanks)
  Cylinder - 2” dia x 24” stroke
    Energy Capacity used = 4524
  Compressor can replace 160 per second at 60 psig
Conclusion: It will take 6.85 to 28.3 seconds to replace the energy used by one activation

## Slide 17: Managing Pneumatic Energy Capacity
Managing the Loss of Energy
  Use only the amount of energy required, not too much more - WHY?
  Minimize Volume:
    tubing length - valve to cylinder
    cylinder stroke
    cylinder diameter
  Minimize regulated pressure
    But, keep above valve pilot pressure requirement

## Slide 18: Optimize Cylinder Stroke, Diameter and Pressure
Stroke
  Shorter stroke => less leverage for angled movement
  Shorter stroke => less weight for cylinder
Diameter
  Smaller diameter => more pressure required for same force
  Smaller diameter => less weight for cylinder
Pressure
  Less pressure => need a bigger, heavier cylinder
  Less pressure => less likely to leak

## Slide 19: Power Experiment
Purpose: Determine Force and Power curves for a pneumatic cylinder
Set-up:
  8” stroke by 1.5” diameter cylinder
  All data taken at 60 psig
  Time recorded to fully extend or contract (8.0”)
    Electronic sensor used at both ends of stroke for timing accuracy
Pull Configuration
Push Configuration
Weight
Cylinder
Table
Pulley

## Slide 20: Force Values
Notes: FIRST did the pneumatic math for us!
We can see here the various force values associated with each bore size, for varying applied pressures.
The relationships are just as we discussed before.

## Slide 21: Cylinder / System Hysteresis
Force
Regulated Pressure
Exerting force
Resisting force
Actuation hysteresis is very pronounced due to:
  Internal cylinder and flow friction
  This can be bad, cannot move objects at rated force - design for this
  This could be good, if leakage occurs and pressure drops slightly, the cylinder will still hold

## Slide 22: Pneumatic Power
Force versus time curve was non-linear as expected
Experimental setup was not perfect, some variation in data expected
  Some friction in cable system
  Ran several times for each weight and took average
Max force that could move was typically less than 85% of theoretical max force

## Slide 23: Pneumatic Power
This pneumatic cylinder systems is not as powerful as better motors in our KOP
  1.5” cylinder ~= 80 watts
  FP motor ~= 171 watts
  CIM motor (small) ~= 337 watts
How do we deal with non-linear behavior?
  Design for the max force to occur before the “knee” in the curve

## Slide 24: Pneumatic Power
I said “1.5” cylinder ~= 80 watts”
Is this True?
What determines the power capacity of a cylinder?
Is it limited by:
Length of the cylinder
Diameter of the cylinder
Max flow rate of the system
The max pressure set on the regulator
It is determined by the amount of energy that can be injected into the cylinder - NOT the cylinder parameters
No
  No
Yes
Yes

## Slide 25: Summary
Pneumatics systems are analogous to electrical systems except for the extra non-linear behavior
Force capacity is determine solely by pressure and cylinder diameter
  The theoretical rated force can be held but not moved
Energy usage is determine by pressure and cylinder volume
The entire system design determines the power capacity of any cylinder
It is easy to run out of pneumatic energy when large cylinder volumes are used
Your compressor most likely does not perform to published specs - do some experiments

## Slide 26: Pneumatics vs. DC Motors Some, but not all important differences
You are allowed to use as many cylinders as you like
  However, you are limited in the types and sizes of cylinders allowed
  You are limited to the KOP Motors
Most of what you need for the pneumatic system is provided in the KOP or easily ordered
Motors have to be geared to produce the desired forces
  Cylinder size can just be picked for the forces you need
Pneumatics are best suited for linear motion
  Motors are best suited for angular motion

## Slide 27: Pneumatics vs. DC Motors Some, but not all important differences
Our ability to control the position of mechanisms actuated by cylinders is very limited
  We are not given integrated, dynamic airflow or pressure controls
  We are given much more versatile electronic controls for motors
Cylinders can be stalled without damage to the pneumatic system
  Motors will draw large current and let out the magic smoke
Cylinders absorb shock loads rather well and bounce back
  However, be careful of over pressure conditions caused by flow control valves
Motors have to be actively held with feedback controls or locked

## Slide 28: Pneumatics vs. DC Motors Some, but not all important differences
Cylinders use up their power source rather quickly
  The 4 air tanks we are allowed do not hold much work capacity
  Motors use up very little of the total capacity of the battery
The decision to use Pneumatics
  The initial investment in weight is great - mostly due to compressor
  Otherwise, very limited air capacity if leave compressor off robot
  Once invested use for as many applications as feasible
    Easy to add more functionality
Cylinders used with single solenoid valves are great for Armageddon devices - stuff happens when power is shut off
  This could be good or bad - use wisely